## Slide 1
ESP32 Embedded Systems Workshop
From Registers to IoT — Learn. Build. Deploy.
2 Days • 10 Hours • 12 Modules • PlatformIO + ESP-IDF • 11:00 AM – 5:00 PM
TM

## Slide 2
01
DAY 1
Foundations
& Sensing
GPIO • Interrupts • ADC - DAC &PWM • EEPROM
8
Modules
5
Hours
18+
Exercises
2
Bare Metal Codes

## Slide 3
Day 1 — Schedule at a Glance
Foundations & Sensing • 11:00 AM – 5:00 PM
11:00 – 11:20
Welcome & Kit Setup
Icebreaker, team formation, PlatformIO check
11:20 – 12:20
Module 1 — Getting Started
ESP32 architecture, GPIO, PlatformIO, first code
12:20 – 13:00
Module 2 — Digital I/O & Interrupts
Polling vs ISR, IR sensor, Tachometer
13:00 – 13:45
Module 3 — Bare Metal & Registers
ESP-IDF, datasheet reading, register programming
13:45 – 14:30
Lunch Break
14:30 – 15:15
Module 4 — Analog Sensing (ADC)
LDR, voltage divider, 12-bit ADC, light zones
15:40 – 16:00
Module 6 — DAC & Output Control
DAC Resolution, wave generation, Audio
16:00 – 16:30
Module 7 — DHT11 & Protocols
Single-wire protocol, temperature alerts
16:45 – 17:00
Day 1 Recap & Quiz
5 rapid-fire questions + Day 2 preview
15:15 – 15:40
Module 5 — PWM & Output Control
LED brightness, LEDC API, tone generation
16:30 – 16:45
Module 8 — EEPROM
Save your data permanently

## Slide 4
OPENING
What is an Embedded System?
The computers hiding inside everything around you
🚗
ABS Brakes
Reads wheel sensor 1000×/sec
📱
Smartphone
10+ microcontrollers inside
🚦
Traffic Light
State machine + timers
🧺
Washing Machine
Sensor fusion + motor control
⌚
Smartwatch
BLE + sensors + power mgmt
🏠
Smart Thermostat
Exactly what you'll build today!
Today's goal: Understand every layer — from silicon registers to Wi-Fi web servers.

## Slide 5
1
DAY 1
MODULE 1
Getting Started
with ESP32
Architecture • GPIO • PlatformIO • Your First Program
ESP32 Embedded Systems Workshop

## Slide 6
MODULE 1
ESP32 Architecture
Why this chip dominates the IoT and embedded world
⚡
Dual-Core Xtensa LX6
240 MHz — Core 0: OS/Wi-Fi Stack | Core 1: Your Code
🧠
Memory
520 KB SRAM • 4 MB Flash • 8 KB RTC RAM (survives deep sleep)
📡
Connectivity
Wi-Fi 802.11 b/g/n • Bluetooth 4.2 & BLE — both built-in
🔌
Peripherals
34 GPIO • 12-bit ADC • DAC • SPI / I2C / UART / I2S
ESP32 vs Arduino UNO
Feature
ESP32
UNO
CPU
240 MHz
16 MHz
RAM
520 KB
2 KB
Flash
4 MB
32 KB
Wi-Fi
✅ Built-in
❌ None
ADC
12-bit
10-bit
Price
~₹260
~₹440
⚠ 3.3V ONLY — GPIO pins are NOT 5V tolerant. Connecting 5V directly causes permanent damage.

## Slide 7
MODULE 1
GPIO Pinout & PlatformIO Setup
Know your board before writing a single line of code
GPIO Pin Categories
GPIO 0,2,4,5,12–19,21–23,25–27,32–33
General Purpose — Input & Output
GPIO 34, 35, 36, 39
Input ONLY — no output capability
GPIO 0, 2, 5, 12, 15
Strapping pins — affect boot mode
GPIO 32–39 (ADC1)
ADC safe even when Wi-Fi is ON ✅
GPIO 4,0,2,15,13,12,14,27,33,32
Capacitive Touch Pins T0–T9
platformio.ini — Project Config
[env:esp32dev]
platform = espressif32
board = esp32dev
framework = arduino
monitor_speed = 115200
; Add libraries here:
lib_deps =
adafruit/DHT sensor library
LED Resistor = (3.3V − 2.0V) ÷ 0.010A = 130Ω → use 220Ω
Exercises:
1.1 Serial Hello
1.2 LED Blink
1.3 Button INPUT_PULLUP
1.4 Button Toggles LED

## Slide 8
2
DAY 1
MODULE 2
Digital I/O &
Interrupts
Polling vs ISR • IR Sensor • Hardware-Driven Response
ESP32 Embedded Systems Workshop

## Slide 9
MODULE 2
Polling vs Hardware Interrupts
The most important concept in real-time embedded systems
❌ Polling — The Wrong Way
void loop() {
// CPU stuck here:
while(digitalRead(IR)==HIGH){
// doing NOTHING else
}
triggerAlert();
}
CPU burns 100% checking a pin that rarely changes.
Cannot read sensors, serve web pages, or do anything else simultaneously.
✅ Interrupt — The Right Way
volatile bool flag = false;
void IRAM_ATTR onIR() {
flag = true; // short ISR!
}
void setup() {
attachInterrupt(IR, onIR, FALLING);
}
CPU is free to do other work. Hardware calls the ISR instantly when event occurs — no polling needed.
ISR Rules: IRAM_ATTR • Keep it SHORT • No Serial.print() • No delay() • volatile for shared vars

## Slide 10
MODULE 2 — EXERCISES
Hands-On Exercises
Ex 2.1
IR Sensor — Polling First
Wire IR to GPIO 14. Poll in loop, print Object/Clear. Feel how it blocks everything.
Ex 2.2
Interrupt-Driven IR + LED
Rewrite using attachInterrupt(). volatile bool flag. LED ON for 2s on detection.
Mini Project 2.3 — RPM Counter
1
LED blinks at
500ms interval
2
Buzzer beeps if RPM>1000
3
Serial: ‘RPM:X'
→
→

## Slide 11
3
DAY 1
MODULE 3
Bare Metal &
Register Programming
ESP-IDF • Datasheet Reading • Direct Hardware Control
ESP32 Embedded Systems Workshop

## Slide 12
MODULE 3
The Abstraction Stack
Every Arduino function is a wrapper — today you go under the hood
YOUR CODE
digitalWrite(GPIO_NUM_2, HIGH);
What you write in Arduino / PlatformIO
↓
ESP-IDF HAL
gpio_set_level(GPIO_NUM_2, 1);
Hardware Abstraction Layer by Espressif
↓
REGISTER OPS
GPIO_OUT_REG |= (1 << 2);
Direct memory-mapped I/O — what you write TODAY
↓
SILICON
Transistor gate → 3.3V on pin
Physics — voltage on the copper trace
Why learn this? Safety-critical systems (automotive, medical, aerospace) require understanding every layer beneath your code.

## Slide 13
MODULE 3 — BARE METAL
Datasheet Reading & Register Exercises
Open the ESP32 Technical Reference Manual — Chapter 4: GPIO
Key GPIO Registers (from TRM Chapter 4)
GPIO_OUT_REG
0x3FF44004
Set output value GPIO 0–31
GPIO_ENABLE_REG
0x3FF44020
Enable GPIO 0–31 as output
GPIO_IN_REG
0x3FF44038
Read input state GPIO 0–31
GPIO_OUT_W1TS_REG
0x3FF44008
Write 1 → SET specific bits
GPIO_OUT_W1TC_REG
0x3FF4400C
Write 1 → CLEAR specific bits
📖 Your Datasheet Task — Find these answers in TRM
1. Address of GPIO_OUT_REG?
2. Which bit position controls GPIO2?
3. How to enable GPIO2 as output?
4. Address & bit for GPIO15 input?
Ex 3.1 + 3.2 — Fill the Blanks
// Ex 3.1 — LED Blink (ESP-IDF)
#define GPIO_OUT_REG \
(*(volatile uint32_t*)0x3FF44004)
#define GPIO_ENABLE_REG \
(*(volatile uint32_t*)0x3FF44020)
void app_main(void) {
// TODO: Enable GPIO2 output
GPIO_ENABLE_REG |= _____;
while(1) {
GPIO_OUT_REG |= _____; // HIGH
vTaskDelay(500/portTICK_MS);
GPIO_OUT_REG &= _____; // LOW
}
}
// Ex 3.2 — Button Read (GPIO_IN_REG)
// Read bit 15 WITHOUT digitalRead()
if (!((GPIO_IN_REG >> ___) & 1)) {
// button pressed — toggle LED
}

## Slide 14
LUNCH
45 minutes • Back at 14:30 sharp

## Slide 15
4
DAY 1
MODULE 4
Analog Sensing
& ADC
LDR • Voltage Divider • 12-bit Precision • Light Zones
ESP32 Embedded Systems Workshop

## Slide 16
MODULE 4
Analog-to-Digital Conversion (ADC)
The real world is analog — ESP32's 12-bit ADC bridges the gap
12-Bit Resolution
0–3.3V in 4096 steps = 0.8mV per step
Arduino UNO = 10-bit (1024 steps — 4× less precise)
ADC1 vs ADC2 ⚠
ADC2 conflicts with Wi-Fi — ALWAYS use ADC1
Safe pins: GPIO 32–39 (ADC1 channels only)
Voltage Divider
LDR + 10kΩ = divider. Bright → LDR low → V rises
Vout = Vsupply × R_fixed ÷ (R_LDR + R_fixed)
Exercises
4.1
Raw LDR + Serial Plotter
GPIO34. Print raw. Use PlatformIO Plotter for live graph.
4.2
Map to Light %
map(raw,0,4095,0,100). Print 'Light Level: 73%'
4.3
Mini: Smart Street Light
BRIGHT>70%: LEDs off | DIM 30–70%: 1 LED | DARK<30%: all LEDs + buzzer on state change
int raw = analogRead(34); // 0 – 4095
int pct = map(raw, 0, 4095, 0, 100); // 0 – 100%
Serial.printf("Light: %d%% | Raw: %d\n", pct, raw); // print both

## Slide 17
5
DAY 1
MODULE 5
PWM & Output
Control
LEDC API • LED Dimming • Tone Generation • Duty Cycle
ESP32 Embedded Systems Workshop

## Slide 18
MODULE 5
PWM — Pulse Width Modulation
Simulate analog output with digital switching — hardware-accurate, zero CPU overhead
Duty Cycle = ON_time ÷ Period × 100%
0%
0
25%
64
50%
128
75%
192
100%
255
ESP32 LEDC API (PlatformIO / Arduino)
ledcSetup(0, 5000, 8); // ch, freq Hz, bits
ledcAttachPin(2, 0); // GPIO, channel
ledcWrite(0, 128); // ch, duty (0-255)
// For buzzer tones (same API!):
ledcWriteTone(1, 523); // ch, frequency Hz
Exercises
5.1
Smooth LED Fade
0→255→0 loop, breathing effect
5.2
Button Brightness Steps
0%→25%→50%→75%→100%→0% each press
5.3
Tone Scale
523Hz C5, 659Hz E5, 784Hz G5 — boot jingle
5.4
Mini: LDR Auto-Dimmer
Bright env = dim LED. Dark = bright. Continuous, no thresholds.

## Slide 19
6
DAY 1
MODULE 6
DAC & Output
Control
Tune Analog Output • 8-bit Resolution • Sine Waves • Audio
ESP32 Embedded Systems Workshop

## Slide 20
MODULE 6
DAC — Digital to Analog Converter
ESP32's built-in DAC produces TRUE analog voltage — no switching, no PWM approximation
ESP32 DAC — Key Facts
Channels:
2 independent DACs — DAC1 & DAC2
Pins:
DAC1 = GPIO 25 | DAC2 = GPIO 26
Resolution:
8-bit → 256 steps (0 = 0V, 255 = 3.3V)
Step Size:
3.3V ÷ 255 ≈ 12.9 mV per step
DAC vs PWM — When to Use Which?
Property
DAC ✅
PWM
Output Type
TRUE analog voltage
Digital pulses (fake analog)
Smoothness
Perfectly smooth signal
Has ripple / switching noise
Best for
Audio, sine waves, sensors
LED dim, motor speed, buzzers
CPU Load
Zero — hardware peripheral
Zero — LEDC hardware timer
Resolution
8-bit (256 steps)
Up to 16-bit (65536 steps)
dacWrite() API — Simple & Direct
// Basic usage — one line!
dacWrite(25, 128); // GPIO25 → 1.65V
dacWrite(26, 0); // GPIO26 → 0.0V
dacWrite(25, 255); // GPIO25 → 3.3V
// Sweep (simple analog ramp):
for (int v=0; v<=255; v++) {
dacWrite(25, v);
delayMicroseconds(500);
}
Advanced: Sine Wave Generation
#include <math.h>
// Generate 1Hz sine wave centered at 1.65V
void loop() {
for (int i=0; i<360; i++) {
float rad = i * (PI / 180.0);
int val = 128 + (int)(127*sin(rad));
dacWrite(25, val); // 0–255
delayMicroseconds(2778); // ~1Hz
}
}

## Slide 21
7
DAY 1
MODULE 7
DHT11 & Sensor
Protocols
Single-Wire • Temperature • Humidity • Error Handling
ESP32 Embedded Systems Workshop

## Slide 22
MODULE 7
DHT11 — Sensor Communication Protocols
Why digitalRead() can't decode a DHT11 — and how libraries solve it
Protocol Landscape
UART
Async serial, 2 wires
SPI
High-speed, 4 wires
I2C
2 wires, multi-device
1-Wire
1 data wire, slow
DHT11 ← YOU ARE HERE
Custom 1-wire, 40-bit, ~70µs timing
DHT11 Specs
Temp Range:
0–50°C (±2°C)
Humidity:
20–80% (±5%)
Sample Rate:
Max 1 reading / second
Data Frame:
40 bits: Humi + Temp + Checksum
// platformio.ini → lib_deps = adafruit/DHT sensor library
#include <DHT.h>
DHT dht(4, DHT11); // GPIO4
dht.begin();
float t = dht.readTemperature();
float h = dht.readHumidity();
if (isnan(t) || isnan(h)) { /* handle error! */ }
float hi = dht.computeHeatIndex(t, h, false);
Ex 7.1 — Read + display Temp/Humidity/HeatIndex every 2s
Ex 7.2 — Mini Project: 3-zone alert (<20°C BLUE | 20-35°C GREEN | >35°C RED + Buzzer alarm)

## Slide 23
8
DAY 1
MODULE 8
EEPROM —
Persistent Memory
Non-Volatile Storage • Wear Leveling • Key-Value Data
ESP32 Embedded Systems Workshop

## Slide 24
MODULE 7
EEPROM — Saving Data That Survives Power Loss
Write once, read forever — persists across resets, deep sleep, and power cuts
What is EEPROM on ESP32?
Not Real EEPROM
ESP32 has no physical EEPROM chip — the library
emulates it using a 4 KB region of SPI Flash.
512 Bytes Default
EEPROM.begin(512) — allocates up to 512 bytes.
Each address stores one byte (0–255).
Wear Leveling
Flash cells die after ~100,000 write cycles.
Avoid writing in tight loops — batch your writes!
commit() is Key
EEPROM.write() only changes the RAM buffer.
EEPROM.commit() physically saves to flash.
EEPROM API — Read & Write
#include <EEPROM.h>
EEPROM.begin(512); // allocate 512 bytes
// ── WRITE ──────────────────────────
EEPROM.write(0, 42); // addr 0 = 42
EEPROM.put(4, 3.14f); // float at addr 4
EEPROM.commit(); // MUST call this!
// ── READ ───────────────────────────
int val = EEPROM.read(0); // → 42
float f;
EEPROM.get(4, f); // → 3.14
Exercises
8.1
Boot Counter —
Count reboots, store in EEPROM addr 0. Print on start.
8.2
Save LED State —
Button toggles LED. Save ON/OFF to EEPROM — persists after reset.
8.3
Sensor data Store —
Write name + threshold float. Read back and print on boot.
💡 EEPROM vs Preferences library: For larger data or key-value pairs, use Preferences.h (NVS) instead — more wear-resistant and easier to use.

## Slide 25
Day 1 — Rapid Fire Quiz
Teams answer on paper — fastest correct team wins 🍫
Q1
What is the memory address of GPIO_OUT_REG on ESP32?
Q2
Which ADC channel group must you avoid when using Wi-Fi?
Q3
What does the volatile keyword mean in the context of an ISR?
Q4
PWM is ON for 2ms in a 10ms period — what is the duty cycle?
Q5
Name ONE reason why delay() is dangerous in real embedded systems.
🚀 Tomorrow: Your ESP32 connects to Wi-Fi. Your phone becomes a remote control.