## Slide 1
ESP32 Embedded Systems Workshop
From Registers to IoT — Learn. Build. Deploy.
2 Days • 10 Hours • 12 Modules • PlatformIO + ESP-IDF • 11:00 AM – 5:00 PM
TM

## Slide 2
02
DAY 2
Connectivity, IoT
& The Challenge
millis() • Deep Sleep • IoT Web Server • Team Algorithm Sprint
4
Modules
75 min
Challenge
3
Problems
1st
Team Wins

## Slide 3
Day 2 — Schedule at a Glance
Connectivity & IoT • 11:00 AM – 5:00 PM
11:00 – 11:15
Day 1 Recap & Warm-Up
millis() warm-up question, quiz answers
11:15 – 12:00
Module 9 — Advanced Peripherals
millis() non-blocking, Hall sensor, Touch pins
12:00 – 12:30
Module 10 — Power Management
Deep Sleep, timer wakeup, GPIO wakeup, RTC memory
13:30 – 14:45
Module 9 — IoT & Web Server
Wi-Fi, HTTP, live dashboard, remote control
14:45 – 15:00
Challenge Briefing & Rules
Problem statements revealed at 15:00 sharp
15:00 – 16:30
🏆 Team Challenge Sprint
All 3 challenges — first to complete all 3 wins
16:30 – 17:00
Results, Prizes & Closing
Trophy ceremony, what's next, resource pack
12:30 – 13:00
Module 11 — RTC
Internal Real Time Clock
13:00 – 13:30
Module 12 — SPIFFS
Internal File system inside flash memory
14:00 – 14:45
Lunch Break

## Slide 4
9
DAY 2
MODULE 7
Advanced Peripherals
& millis()
Non-Blocking Code • Hall Effect • Capacitive Touch
ESP32 Embedded Systems Workshop

## Slide 5
MODULE 7
Non-Blocking Code with millis()
delay() kills your firmware — millis() sets it free
❌ delay() — CPU is DEAD
void loop() {
// Can't read sensors
// Can't serve web pages
// Can't handle buttons
digitalWrite(LED, HIGH);
delay(1000); // CPU DEAD here
digitalWrite(LED, LOW);
delay(1000);
}
✅ millis() — CPU stays ALIVE
unsigned long prev = 0;
bool state = false;
void loop() {
if (millis() - prev >= 1000) {
prev = millis();
state = !state;
digitalWrite(LED, state);
}
// CPU free for anything!
}
Hall Effect Sensor (Built-In!)
No wiring needed — built into ESP32 chip.
hallRead() → returns field strength.
Bring phone near chip — watch value change.
Capacitive Touch Pins T0–T9
Wire 15cm jumper to GPIO4 (T0) as antenna.
touchRead(T0) → ~60 idle, ~10 when touched.
No mechanical parts — touchless switch!

## Slide 6
10
DAY 2
MODULE 8
Power Management
& Deep Sleep
10µA Sleep • Timer Wakeup • GPIO Wakeup • RTC Memory
ESP32 Embedded Systems Workshop

## Slide 7
MODULE 8
Deep Sleep — Making IoT Devices Last
Active: 240mA vs Deep Sleep: 0.01mA = 1000× longer battery life
ESP32 Power Modes
Active
~240 mA
Full speed — Wi-Fi, CPU, peripherals
Modem Sleep
~20 mA
CPU runs, Wi-Fi off between TX
Light Sleep
~2 mA
CPU paused, RAM retained
Deep Sleep
~0.01 mA
Only RTC — 1000× battery savings ✅
Exercises
RTC_DATA_ATTR int bootCount = 0;
void setup() {
bootCount++;
Serial.printf("Boot #%d\n",bootCount);
// ...read sensor, blink LED...
esp_sleep_enable_timer_wakeup(
10ULL * 1000000); // 10 seconds
esp_deep_sleep_start();
}
Ex 8.1 — Timer Wakeup:
Blink LED, sleep 10s, wake, print boot count (RTC_DATA_ATTR survives sleep), repeat.
Ex 8.2 — GPIO Button Wakeup (EXT0):
Sleep until GPIO15 button pressed → wake → read DHT11 → print temp → sleep again. This is how smart door sensors work.
Real Math: Every 5min active — 3s @ 240mA + 297s @ 0.01mA = avg 2.4mA → 2000mAh battery lasts 34 days vs 8 hours without sleep.

## Slide 8
11
DAY 2
MODULE 8
RTC — Real
Time Clock
Timekeeping • Alarms • Timestamps
ESP32 Embedded Systems Workshop

## Slide 9
MODULE 8
RTC — Real Time Clock
Track time using the ESP32's built-in RTC — no extra hardware needed, powered by the same chip
How the Internal RTC Works?
Clock Source
RTC runs on a 150 kHz internal oscillator (or external 32.768 kHz crystal if fitted)
Survives Deep Sleep
The RTC domain stays powered even in deep sleep (~6.5 µA) — time keeps ticking
Does NOT survive power-off
No battery backup — loses time if 3.3V is removed completely
Setting Time: Two Methods
Method
Use When
configTime() + NTP
Wi-Fi available — syncs from internet, most accurate
struct tm manual set
No Wi-Fi — hardcode date/time at upload
RTClib Code — Set, Read & Alarm
// platformio.ini — no extra lib_deps needed!
#include <WiFi.h>
#include "time.h"
const char* ntpServer = "pool.ntp.org";
const long gmtOffset = 19800; // IST = UTC+5:30 (seconds)
const int daylightOffset = 0;
void setup() {
Serial.begin(115200);
WiFi.begin("SSID", "PASSWORD");
while (WiFi.status() != WL_CONNECTED) delay(500);
// Sync time from internet
configTime(gmtOffset, daylightOffset, ntpServer);
}
void loop() {
struct tm timeinfo;
if (!getLocalTime(&timeinfo)) {
Serial.println("Failed to get time");
return;
}
// Print formatted date & time
Serial.printf("%04d/%02d/%02d %02d:%02d:%02d\n",
timeinfo.tm_year + 1900,
timeinfo.tm_mon + 1,
timeinfo.tm_mday,
timeinfo.tm_hour,
timeinfo.tm_min,
timeinfo.tm_sec);
delay(1000);
}
Ex 8.1 — Log DHT11 readings with timestamp: "2025/03/08 14:32:05 | Temp: 28.4°C | Hum: 62%“
Ex 8.2 — Trigger buzzer alarm at a specific hour:minute using timeinfo.tm_hour and timeinfo.tm_min
Drift
~1–2 minutes per day — acceptable for logging; use NTP sync over Wi-Fi for precision
Resolution
1 second via getLocalTime(), microseconds via esp_timer_get_time()

## Slide 10
12
DAY 2
MODULE 9
SPIFFS —
File System Storage
Flash File System • Config Files • Logging
ESP32 Embedded Systems Workshop

## Slide 11
MODULE 9
SPIFFS — Serial Peripheral Interface Flash File System
Store HTML, config files, images, and data logs directly on the ESP32's own flash chip
What is SPIFFS?
What is SPIFFS?
Flash Partition
Uses unused portion of the 4 MB Flash chip
alongside your code — typically 1–3 MB available.
Flat File System
No folders — files live at paths like /index.html
/config.json /data.csv /logo.png
Use Cases
Serve HTML/CSS/JS from ESP32 as web server,
store sensor logs, save config settings as JSON.
Storage Options — Quick Comparison
Type
Size
Access
Best For
EEPROM
~512 B
Bytes
Settings, flags
SPIFFS
1–3 MB
Files
HTML, logs, JSON
SD Card
GB+
Files
Large data logging
SPIFFS API — Read, Write & List Files
#include <SPIFFS.h>
SPIFFS.begin(true); // true = format if needed
// ── WRITE a file ────────────────────
File f = SPIFFS.open("/config.txt", "w");
f.println("threshold=35");
f.println("name=ESP32_Node1");
f.close();
// ── READ a file ─────────────────────
File f2 = SPIFFS.open("/config.txt","r");
while (f2.available()) {
Serial.println(f2.readStringUntil('\n'));
}
f2.close();
// ── LIST all files ──────────────────
File root = SPIFFS.open("/");
File entry = root.openNextFile();
while (entry) {
Serial.printf("%s %d bytes\n",
entry.name(), entry.size());
entry = root.openNextFile();
}
Ex 9.1 — Write + read a config.txt file
Ex 9.2 — Log DHT11 readings with timestamps to /log.csv

## Slide 12
9
DAY 2
MODULE 9
IoT &
Web Server
Wi-Fi Modes • HTTP Server • Live Dashboard • Remote Control
ESP32 Embedded Systems Workshop

## Slide 13
MODULE 9
ESP32 Wi-Fi & HTTP Server
STA Mode • AP Mode • HTTP Request/Response • Remote Control
Wi-Fi Modes
STA (Station)
Connects TO existing Wi-Fi. Gets IP from router.
AP (Access Point)
Creates its OWN hotspot. Phone connects to ESP32 directly.
STA+AP (Both)
Connected to router AND hosting hotspot simultaneously.
HTTP Request / Response Cycle
1
Browser sends:
GET /sensor HTTP/1.1
2
ESP32 receives:
server.handleClient()
3
ESP32 responds:
HTML with sensor values
4
Browser renders:
Your dashboard appears!
⚠ ADC2 + Wi-Fi Conflict: GPIO 0,2,4,12-15,25-27 unreliable when Wi-Fi is ON — always use ADC1 (GPIO 32-39).
WiFi.begin("WorkshopSSID", "password");
while (WiFi.status() != WL_CONNECTED) { delay(500); }
Serial.println(WiFi.localIP()); // e.g. 192.168.1.105 — open in phone browser!
server.on("/", handleRoot); server.on("/led/on", handleLEDon); server.begin();

## Slide 14
MODULE 9 — EXERCISES
Building Your IoT Dashboard
From 'Hello World' to live sensor control — step by step
Ex 9.1
Connect to Wi-Fi & Get IP
Connect to workshop Wi-Fi. Print IP. Open http://[IP] in phone browser.
Ex 9.2
Serve a Web Page
Return <h1>Hello from ESP32!</h1>. Style with inline CSS. View in browser.
Ex 9.3
Live Sensor Dashboard
Auto-refresh every 3s. Show Temp, Humidity, Light%, Motion with color coding.
Ex 9.4
Remote Hardware Control
Add [LED ON] [LED OFF] [Buzz] buttons. Click in browser → hardware responds.
🌐 Ex 9.5 — Complete IoT Dashboard
All sensor readings live
Auto-refresh every 3s
LED ON/OFF + Buzz buttons
Uptime counter via millis()
NORMAL / ALERT status indicator
1
4
2
5
3

## Slide 15
LUNCH
45 minutes • Back at 14:45 sharp
🏆 THE CHALLENGE BEGINS AT 15:00
Review your code • Discuss strategy • Refresh the concepts
No AI tools during the challenge — documentation only!

## Slide 16
🏆 THE TEAM CHALLENGE
Algorithm & Logic Sprint • 33 Teams • 75 Minutes
FORMAT: Complete all 3 challenges in sequence (C1 → C2 → C3)
First team to have all 3 judge-verified wins. Ranked by: challenges completed → time of last judge stamp.
✅ Internet docs ALLOWED
Datasheets, Arduino reference, Stack Overflow — use them!
🚫 No Generative AI
ChatGPT, Copilot, Gemini banned — violation = disqualification
🔩 Kit components only
No external libraries beyond workshop-used ones
🗣️ Every member must explain
Judge will ask any member about any part of the code
⚖️ Judge's call is final
Demo must work on demand — not just once in the past
⏰ Problems revealed at 15:00 — CLOCK STARTS

## Slide 17
CHALLENGE 1
The Watchdog
State Machine + Interrupt Logic • Est. 12–18 min for fast teams
3-State System — Must behave EXACTLY as described:
State
Trigger Condition
LED Behavior
Buzzer
🔴 IDLE
System start / after button reset
Slow blink 1s ON / 1s OFF
Silent
🔴 WARNING
IR detects object
Fast blink 200ms ON / 200ms OFF
Single beep every 2s
🔴 ALARM
IR detected > 5 continuous seconds
Solid ON — no blink
Rapid beep 100ms/100ms
Additional Rules
All timing via millis() — NO delay() anywhere
Button = RESET interrupt (any state → IDLE)
Serial prints every transition: 'STATE: WARNING→ALARM | T=12340ms'
Object removed in WARNING before 5s → back to IDLE
Judge Verification
Trigger IR → verify WARNING blink rate
Hold IR 6s → verify ALARM escalation
Press button → verify IDLE reset
Check Serial for correct transition logs
Q: Draw the state machine diagram now

## Slide 18
CHALLENGE 2
The Vault
Sequential Lock Algorithm • Pattern Recognition • Timeout Logic • Est. 18–25 min
Unlock Sequence — Must match EXACTLY:
1
Step 1 — LDR
Cover LDR — hold for 1+ second (light < threshold)
2
Step 2 — IR
IR detects object — within 3s of Step 1 completing
3
Step 3 — Button
Press button — within 3s of Step 2 completing
System Responses:
Correct step:
LED blinks once (100ms) — acknowledgement
Step timeout:
Descending 3-tone alert → reset to Step 1
Wrong order:
Double-beep → immediate reset to Step 1
Full sequence ✅:
LED solid + ascending melody + 'VAULT UNLOCKED | Xms'
Must Also Track:
Attempt count (total tries)
Success count (unlocks)
Time of each step via millis()
3s window accurate to ±100ms
Judge Verification:
Deliberate wrong sequence → must reject
Let step timeout → alert + reset
Correct full sequence → must unlock
Judge times 3s window with phone
Q: 'What tracks the current step?'

## Slide 19
CHALLENGE 3
The Reactor
Sensor Fusion • Scoring Algorithm • Proportional Response • Est. 20–30 min
Threat Score Algorithm — Implement EXACTLY:
THREAT_SCORE = 0
IF temp > 35°C → SCORE += 40
IF temp 30–35°C → SCORE += 20
IF light < 20% → SCORE += 30
IF light 20–40% → SCORE += 15
IF IR detects motion → SCORE += 30
RANGE: 0 – 100
Response by Score:
0 – 30
SAFE
Green LED solid
Silent
31 – 60
CAUTION
Green LED fast blink
Beep every 3s
61 – 100
CRITICAL
All LEDs rapid blink
Continuous beep
Additional Rules:
Score recalculated every 500ms using millis()
Serial: 'SCORE: 70 | CRITICAL – HIGH_TEMP, DARK, MOTION'
Boundary crossings: ascending tones up, descending down
No delay() anywhere in the code
Judge Verification:
Cover LDR → score changes
Breathe on DHT11 → temp rises → score changes
Trigger all 3 → must hit CRITICAL
Judge asks team to predict score before each change
Q: 'How would you add a 4th sensor?'

## Slide 20
Scoring, Rankings & Prizes
First team verified on all 3 challenges wins 🏆
Tiebreaker: Both teams finish simultaneously? Judge asks one technical question — better answer wins.
1st Place
First team verified on all 3 challenges
2nd Place
Second team verified on all 3
3rd Place
Third team verified on all 3

## Slide 21
You're Now an Embedded Engineer.
Here's what you built in 10 hours — and where to go next
✓ GPIO & Arduino
pinMode, digitalWrite, digitalRead, interrupts
✓ Bare Metal C
Register addresses, TRM navigation, volatile
✓ Analog (ADC)
12-bit sensing, voltage dividers, thresholds
✓ PWM
LEDC API, LED brightness, tone generation
✓ Protocols
DHT11 single-wire, library-based sensor comms
✓ Power Management
Deep sleep, 1000× battery life, RTC memory
What's Next on Your Embedded Journey:
FreeRTOS
Multitasking
MQTT
Cloud IoT
ESP-IDF
Full Framework
PCB Design
KiCad
OTA Updates
Production
TLS/Security
Encryption
📦 Resource Pack (shared now):
GitHub repo (all exercise code) • ESP32 TRM PDF • PlatformIO quickstart guide • Component datasheets